## Slide 1: Lecture # 3
Flood Routing

## Slide 2
The hydrograph of a flood entering a reservoir will change in shape as it emerges out of the reservoir, because certain volume of its water is stored in the reservoir temporarily and is let off as the flood subsides. The base of the hydrograph, therefore, gets broadened, its peak gets reduced, of course, the time of peak is delayed. A process known as flood routing, and more particularly as reservoir routing (to differentiate it from routing though ‘river channels’) can compute the extent by which the inflow hydrograph gets modified due to the reservoir storage.
FLOOD ROUTING

## Slide 3
Flood routing
It is the process of calculating water levels in reservoir, the storage quantaties and outflow rates corresponding to a particular inflow hydrograph at various instants.
Since the flood protection reservoirs are generally located many km upstream of the cities, which are to be saved against floods, it is sometimes necessary to route the outflow hydrograph of the reservoirs up to these downstream localities. The reservoir outflow hydrograph may then be routed through this much length of river channel, so as to obtain the final shape of the hydrograph at the affected cities. This routing, in which the stream itself acts like an elongated reservoir, is known as channel routing or river routing.

## Slide 4
Hydrologic Reservoir Routing Methods
The passage of a flood wave through a reservoir or a river reach is unsteady flow phenomenon. In hydraulics, we classify it as a gradual varied flow. The equation of continuity used in all the hydrologic routing methods, as the primary equation, states that the difference between inflow and the outflow rate is equal to the rate of change of storage, i.e
I – O = dS/dt
Where, I = Inflow rate , O = Outflow rate, S = Storage, and t = time.
Alternatively, in a small time interval  t, the difference between total inflow volume and the total outflow volume is equal to the change in storage volume.
I  t – O  t =  S

## Slide 5: Continuity Equation in Difference Form
Referring to figure, the continuity equation in difference form can be expressed as

## Slide 6
The inflow flood hydrograph, the elevation-storage curve, and the outflow­ elevation curve respectively represent them. The third relation may be represented by the spillway­ discharge equation (Q = 1.71 LH3/2) only if, the discharge through the outlets is neglected. If the discharge though the outlets is also not neglected, then all the three curves will be not expressed by simple algebraic equations, without drastic assumptions.

## Slide 7
Several procedures have been applied to solve the above equation as follows:
1- trial and error method
2- Modified Pul’s method or storage indication method
2- Goodrich method.
First method is discussed here because it is widely adopted with the assistance of computers to reduce the time taken in long calculations involved in this method. This method arranges the basic routing equation as follows:
I  t = O  t +  S
(I1 + I2)/2 .  t = (O1 + O2)/2 .  t + (S2 – S1)
the procedure involves assuming of a particular level in the reservoir the end of the interval  t, and computing the values on the right side of above Equation. The summation of (O1 + O2)/2 .  t and (S2 – S1) is then compared with the known value of (I1 + I2)/2 .  t. If the two values are the same then the assumed reservoir elevation at the end interval is o.k. Otherwise, the elevation is changed and the process is repeated till required matching is obtained.